## Slide 1
Manual vs. Navigation-Guided
Spine Surgery
Project 2 competitive analysis, workflow mapping, and integration opportunities
Durga Moorthy
October 2026
Scope
Five navigation platforms
Eleven workflow stages
Five instrument categories
Notes: Sources: project2_navigation/competitor_analysis.md; navigation_workflows.md; instrument_taxonomy.md.

## Slide 2
Competitive landscape
Five platforms cover different combinations of imaging, tracking, and robotic guidance
Medtronic
StealthStation
Mature navigation
Multi-specialty
Globus
ExcelsiusGPS
Spine focus
Integrated robotics
Stryker
Navigation platforms
CT and fluoroscopy
Hybrid tracking
Brainlab
Spine Suite
Multi-modal imaging
Modular workflow
7D Surgical
Surgical AI
Markerless tracking
Intraoperative 3D
Comparison focus: platform workflow, registration, tracking, imaging, planning automation, and surgical guidance
Project 2 surgical navigation analysis
2
Notes: Source: project2_navigation/competitor_analysis.md. Platform attributes are a research summary, not a clinical recommendation.

## Slide 3
Platform comparison
The market divides around imaging, tracking reference, and robotic execution
Platform
Planning and imaging
Tracking or registration
Guidance model
StealthStation
CT and fluoroscopy
Optical reference arrays
Navigation display
ExcelsiusGPS
Preoperative CT
Surface reference and optical tracking
Robotic drill guide
Stryker
CT and fluoroscopy
Optical and electromagnetic options
Navigation with hybrid integration
Brainlab
CT, MRI, PET, iCT
Optical and multi-modal registration
Modular navigation and optional robotics
7D Surgical
Intraoperative 3D imaging
Markerless vision registration
Real-time image guidance
Project 2 surgical navigation analysis
3
Notes: Source: project2_navigation/competitor_matrix.csv and competitor_analysis.md.

## Slide 4
Spine navigation workflow
Eleven stages connect preoperative planning with intraoperative guidance and verification
Preoperative planning
1 Assessment
2 Imaging
3 Segmentation
4 Trajectory design
Operative setup and registration
5 Patient setup
6 Registration
7 Instrument calibration
Guidance and verification
8 Guided execution
9 Intraoperative check
10 Closure
11 Postoperative imaging
Project 1 contributes at stages 2–4: CT preprocessing, vertebral segmentation, labeling, and planning inputs
Project 2 surgical navigation analysis
4
Notes: Source: project2_navigation/navigation_workflows.md.

## Slide 5
Instrument and system taxonomy
Navigation depends on a linked chain of patient reference, tracked tools, imaging, and control hardware
1
Reference frames
Patient-mounted arrays
Markerless landmarks
2
Surgical instruments
Probe
Drill guide
Insertion tool
3
Imaging and displays
Fluoroscopy
Cone-beam CT
Navigation monitor
4
Tracking systems
Optical cameras
EM transmitter and sensors
5
Data and control
Planning workstation
Robotic controller
Audit trail
Design implication: segmentation output must align with the CT coordinate system used by registration and instrument tracking
Project 2 surgical navigation analysis
5
Notes: Source: project2_navigation/instrument_taxonomy.md.

## Slide 6
Where automated vertebral segmentation can add value
The largest opportunities sit before and during trajectory planning
Accelerated planning
Auto-segment and label vertebrae before manual planning
High impact
Pathological anatomy
Flag fractures, scoliosis, degeneration, and prior instrumentation
Very high impact
Intraoperative adaptation
Use updated imaging to detect meaningful anatomical shift
High impact
Instrument-aware trajectories
Apply geometry and approach constraints to screw paths
High impact
Project 2 surgical navigation analysis
6
Notes: Source: project2_navigation/opportunity_matrix.csv. Impact labels reflect the project opportunity matrix, not validated clinical outcomes.

## Slide 7
Proposed integration pathway
Project 1 output becomes a structured planning input for navigation workflows
CT volume
Preoperative CT
›
Vertebral masks
3D segmentation
›
Anatomical labels
Centroids and level identity
›
Pedicle geometry
Width, length, orientation
›
Screw plan
Trajectory and dimensions
›
Navigation display
Surgeon review and guidance
Current state: CT preprocessing and the segmentation baseline are implemented. Labeling, pedicle geometry, and screw planning require validated full-split model output.
Project 2 surgical navigation analysis
7
Notes: Sources: docs/technical_architecture.md; project1_vertebra_segmentation/models/baseline_selection.md. Current-state wording reflects repository status as of October 2026.

## Slide 8
Evidence boundaries and risks
The next phase must establish performance before clinical integration claims
Evidence needed before evaluation
Full VerSe training and held-out validation
Per-vertebra Dice, IoU, and HD95
Anatomical labeling accuracy
Inference time on a defined device
Failure analysis for pathology and artifacts
Cases that require targeted testing
Partial field of view
Transitional vertebrae
Scoliosis and severe degeneration
Prior instrumentation and metal artifacts
Scanner and protocol variation
Project 2 surgical navigation analysis
8
Notes: Sources: project1_vertebra_segmentation/literature/literature_review.md; docs/technical_architecture.md; PROJECT_STATUS.md.

## Slide 9
Next steps
A measured path from implementation to validated planning support
1
Full VerSe baseline
Train and evaluate on the official split
2
Failure analysis
Review per-vertebra and pathology-specific errors
3
Pedicle geometry
Extract anatomy needed for trajectory constraints
4
Planning prototype
Generate surgeon-reviewable screw plans
Decisions requested: compute and storage for full training, validation-data access, and the preferred scope for the first pedicle-planning prototype
Project 2 research foundation complete
Notes: Sources: PROJECT_STATUS.md; docs/MEETING_READINESS.md; project2_navigation/opportunity_matrix.csv.

## Slide 10
Intraoperative workflow: official product photograph
Competitive-landscape example of tracking, navigation display, and guided instrumentation
What the visual shows
A tracking-enabled robotic arm, navigation display, and surgical instruments share the sterile field. These are the practical workflow elements studied in the Project 2 comparison: registration, guidance, instrumentation, and verification.
Official Globus Medical product-page visual. Included as an example of a vendor workflow—not as a comparative performance claim or endorsement.
Project 2 surgical navigation analysis
10
Notes: Official image source: Globus Medical, ExcelsiusGPS product page. Image asset: https://www.globusmedical.com/wp-content/themes/globus/images/posters/EGPS/EGPS-navinstruments.webp. Product page: https://www.globusmedical.com/musculoskeletal-solutions/excelsiustechnology/excelsiusgps/

## Slide 11
Official product media and virtual demo
Real imagery and the embedded virtual demonstration from the vendor’s product page
ExcelsiusGPS system setup
Official product-page visual showing the navigation camera, monitor, and robotic platform.
globusmedical.com/.../excelsiusgps/
Official virtual demo
The product page includes an official video demonstration of ExcelsiusGPS spine and interbody solutions.
youtube.com/watch?v=06YapAnXl6A
Project 2 surgical navigation analysis
11
Notes: Official sources: Globus Medical ExcelsiusGPS product page: https://www.globusmedical.com/musculoskeletal-solutions/excelsiustechnology/excelsiusgps/. Official product media assets: https://www.globusmedical.com/wp-content/themes/globus/images/posters/EGPS/EGPS-header-intro.webp and https://www.globusmedical.com/wp-content/themes/globus/images/scrollers/egps/EXCL_GPS_1801_TECH_FINALCONSTRUCT_ExcelsiusGPS_C.webp. Official video embedded on the product page: https://www.youtube.com/watch?v=06YapAnXl6A. The deck links to the video rather than embedding it so it stays portable.